## Slide 1: Shape aware Tracking in Bioimaging
Ahmad Humayun
http://www.cs.ucl.ac.uk/students/A.Humayun/

## Slide 2
Cell motility
Basic techniques in Tracking
Solving for Occlusion in Actin-Myosin motility tracking
Shape aware Tracking in Bioimaging
Notes: -> 2nd part will involve generalized tracking – can be applied to anything

## Slide 3: Cell motility 101
Cytoskeleton (Actin proteins)
Motor proteins (Myosin proteins)
Image used with permission from Charlotte Pratt http://www.wiley.com/college/pratt/0471393878/student/
Notes: -> Cytoskeleton
(1) provides cell a shape
(2) Changing comp. – helps cellular movement & division
(3) Various Motor proteins bind to and move along cytoskeletal comp.
(4) Figure: shows how F-Actin microfilament formed (Actin globular protein). Formed by combining nucleotides ATP by hydrolysis to make chain of ADP nucleotides. ATP responsible for chemical energy in cells for metabolism – a body holds enough ATP to give energy = 1 AA battery – ATP is constantly used in regenerated in cells.
(5) microfilaments - dynamic structures, they help in cellular movement – e.g. white blood cells remodel microfilaments -> cross capallary walls to enter damaged tissue -> wound healing.
-> One Motor proteins is Myosin – moves along Actin proteins (cytoskeletal comp.)
(1) Actin Myosin interaction responsible for muscle contractions
-----------------------------------------------------------------------
Notice how the protein consists of two domains separated by a cleft. Actin is assembled to form long protein polymers called micro-filaments. Polymerized actin is filamentus and is usually called F-Actin.
One form of microfilament movement is treadmilling – when the rate of removal and addition of actin subunits is equal at both ends.

## Slide 4: Motor Proteins
Responsible for movement in cells. Examples:
  Muscle contraction
  Deliver neurotransmitters to nerve cells
  Pulling power needed during cell division
  Deliver energy-producing Mitochondria to cellular neighborhoods
Animation borrowed from http://pubs.acs.org/cen/science/84/8447sci1.html
Notes: -> Vehicles of transportation
-> Motor proteins can travel great distances with great timing
-> Pulling power to separate chromosomes during cell division
-> kinesins walk down nerve cell, make sure axon well stocked neurotransmitters.
-> Transport neurotransmitters up to a 1 meter away
-> Video: See Kinesin transporting

## Slide 5: Myosin Proteins
Myosin head
Myosin neck
F-Actin
Lever arm of Myosin responsible for Power Stroke
Animation used with permission from Charlotte Pratt http://www.wiley.com/college/pratt/0471393878/student/
Notes: -> Microfilaments partnered with motor protein Myosin, tensile force
-> Muscle contraction is done by muscle myosin
-> Myosin proteins, moves over cytoskeletal substrates converting chemical to mechanical
-> The source of chemical energy is ATP.
-> Video: ATP hydrolysis on Myosin head causes this power stroke
(process knows when and how to move your foot’s arch)
-> Figure: Our experiment TURN AROUND Myosin
---------------------------------------------------------------
A series of small conformational changes that are tightly linked to the nucleotide associated events occurs within the protein. The end result is a large conformational change called the power stroke. The end result is the tensile force within a cell.

## Slide 6: Butt et al. 2010 – J. of Bio. Chemistry
Using an in-vitro setup, discovered:
  Orientation of F-actin dependent on filament length and density
  Densities close to mammalian cells gives oriented gliding
Random gliding
Oriented gliding
Notes: -> Previously Orientation dependent on length
-> We studied quantitatively how this orientation come about
Dependence on F-actin length and Density
Interestingly oriented when densities close to Mammalian cells
-> Video: only a certain number of Actins Rhodamine Phalloidin
Why IMPORTANT:
-> F-Actin play an important role in migrating cells.
-> Since their effect stretches far greater than their own length
–techniques where cell migration responds to chemical cues.

## Slide 7
Cell motility
Basic techniques in Tracking
Solving for Occlusion in Actin-Myosin motility tracking
Shape aware Tracking in Bioimaging
Notes: 2nd part will involve generalized tracking – can be applied to anything

## Slide 8
Fn+1
Fn
1
2
3
B
C
A
Most methods correspond detected features between 2 or more frames:
1. Detection of feature points (Bg. Subtraction followed by e.g. centroid, KLT [1])
2. Correspond those feature points across frames ([2], [3])
[1] J. Shi, C. Tomasi, “Good Features to Track,” Proc. IEEE Conf. Computer Vision and Pattern Recognition, 1994.
Point-to-Point Tracking Techniques
[2] C.J. Veenman, M.J.T. Reinders,E. Backer, “Resolving Motion Correspondence for Densely Moving Points,” IEEE Trans. PAMI, 2001.
[3] K. Shafique, M. Shah, “A Noniterative Greedy Algorithm for Multiframe Point Correspondence,” IEEE Trans. PAMI, 2005.
Notes: -> Detection Features
SIFT features
KLT

## Slide 9
a. The correspondence is usually done by solving a bipartite graph
 | A | B | C
1 | 2 | 53 | 38
2 | 41 | 11 | 7
3 | 49 | 5 | 16
Entry |  |  |  | 
Exit
2
7
5
Number of objects might be different in Fn and Fn+1 , hence:
Points from Fn can Exit
Points from Fn+1 can Enter
The points are corresponded by the use of Costs
1. Detection of feature points (Bg. Subtraction followed by e.g. centroid, KLT [1])
2. Correspond those feature points across frames ([2], [3])
[1] J. Shi, C. Tomasi, “Good Features to Track,” Proc. IEEE Conf. Computer Vision and Pattern Recognition, 1994.
[2] C.J. Veenman, M.J.T. Reinders,E. Backer, “Resolving Motion Correspondence for Densely Moving Points,” IEEE Trans. PAMI, 2001.
[3] K. Shafique, M. Shah, “A Noniterative Greedy Algorithm for Multiframe Point Correspondence,” IEEE Trans. PAMI, 2005.
Most methods correspond detected features between 2 or more frames:
Point-to-Point Tracking Techniques
Notes: The Hungarian method solves the assignment problem in polynomial time O(n3)
-> Graph
-> What is the hungarian method?
-> 3 ppl, 3 jobs
Things to note:
-> Different number of objs in frames
-> What values for Exit / entry
-> The COST itself is our key-contribution in the Tracking domain

## Slide 10
Fn
Corresponding through feature points e.g. centroids.
Is this the best approach? Feature points don’t always take the whole object shape into context, affecting tracking.
Fn+1
EXIT ?
Motivation
Notes: -> Figure: show the non-trivial assignment using features

## Slide 11: Motivation
Resolved
Fn+1
How to correspond between regions / objects across a frame?
Fn
Fn+1
Are there added advantages of corresponding whole object shapes rather than points?
Use of shape parameters (and probabilistic models) can result in better correspondence
Questions
Notes: -> We argue, some situations use of shape parameters -> better correspondence
-> Figure illustrate the intuitive idea
What questions does this technique raises:
-> How do we associate one shape to another
-> Added-advantages of using shape for correspondence (OCCLUSIONS)
“not interested in disparate features, rather the shapes that comprise of those features”

## Slide 12: Correspondence Basics
1
2
1
3
4
Possible motion that could occur during a frame transition need to be looked at …
Note the Entry, Exit, Merge and Split amongst the objects
Fn
Notes: -> Across times as objects move –entries, exits, and splits/merges b/w objects.
-> Animation: shows what happens between the 2 frames

## Slide 13: Correspondence Basics
1
B
C
A
D
Possible motion that could occur during a frame transition need to be looked at …
Note the Entry, Exit, Merge and Split amongst the objects
Fn+1

## Slide 14: Correspondence Basics
1 in Fn split to B and C in Fn+1
3 and 4 in Fn merged to D in Fn+1
2 in Fn exited the frame
A entered in Fn+1
The outcome of this frame transition:
A
D
B
C
Fn+1
2
1
3
4
Fn
(Fn) and (Fn+1) are the snapshots in time
How to get the right outcome?
Choose the outcome whose Cost of occurrence is the lowest
Notes: -> We can work with the two frames, (Fn) and (Fn+1) showing a time transition
-> TRICKY PART: is computing the right outcome, we need to look at all the possibilities.
-> Depending on way costs set-up, choose the outcome whose cost of occurrence is the lowest or highest

## Slide 15
Step 1: Cost of individual Fn obj. to Fn+1 obj.
 | A | B | C | D
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 
4 |  |  |  | 
To compute the ANSWER, we need a matrix of costs, which can be resolved by the Hungarian Algorithm
Notes: Step 1: Calculate cost of correspondence of each individual Fn obj. to Fn+1 obj.
Step 2: Calculate cost of correspondence for an Fn obj. splitting to many Fn+1 objs.
Step 3: Similarly compute cost of combining multiple Fn objs. to 1 Fn+1 obj.
Condition: The grey area is irrelevant (e.g. 1,2 can be corresponded to A,B from other matrix cells too).
Step 4: Green column denotes the exiting cost of any Fn obj.
Step 5: Green row denotes the costs of any obj. in Fn+1 entering.
Step 6: The Hungarian algo. will be used to find the minimum cost solution.

## Slide 16
To compute the ANSWER, we need a matrix of costs, which can be resolved by the Hungarian Algorithm
1,2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1,3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1,4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2,3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2,4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
3,4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1,2,3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1,2,4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1,3,4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2,3,4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1,2,3,4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
A,B | A,C | A,D | B,C | B,D | C,D | A,B,C | A,B,D | A,C,D | B,C,D | A,B,C,D
Step 1: Cost of individual Fn obj. to Fn+1 obj.
Step 2: Cost of an Fn obj. splitting to many Fn+1 objs.
Step 3: Cost of combining multiple Fn objs. to 1 Fn+1 obj.
Condition: The grey area is irrelevant!
 | A | B | C | D
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 
4 |  |  |  | 
Notes: Step 1: Calculate cost of correspondence of each individual Fn obj. to Fn+1 obj.
Step 2: Calculate cost of correspondence for an Fn obj. splitting to many Fn+1 objs.
Step 3: Similarly compute cost of combining multiple Fn objs. to 1 Fn+1 obj.
Condition: The grey area is irrelevant (e.g. 1,2 can be corresponded to A,B from other matrix cells too).
Step 4: Green column denotes the exiting cost of any Fn obj.
Step 5: Green row denotes the costs of any obj. in Fn+1 entering.
Step 6: The Hungarian algo. will be used to find the minimum cost solution.

## Slide 17
1,2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1,3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1,4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2,3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2,4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
3,4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1,2,3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1,2,4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1,3,4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2,3,4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1,2,3,4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
A,B | A,C | A,D | B,C | B,D | C,D | A,B,C | A,B,D | A,C,D | B,C,D | A,B,C,D
Entry |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Exit
Step 1: Cost of individual Fn obj. to Fn+1 obj.
Step 2: Cost of an Fn obj. splitting to many Fn+1 objs.
Step 3: Cost of combining multiple Fn objs. to 1 Fn+1 obj.
Condition: The grey area is irrelevant!
Step 4: The green column denotes the exiting cost of any Fn obj.
Step 5: The green row denotes the costs of any obj. in Fn+1 entering.
Step 6: The Hungarian algo. will be used to find the minimum cost solution.
 | A | B | C | D
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 
4 |  |  |  | 
To compute the ANSWER, we need a matrix of costs, which can be resolved by the Hungarian Algorithm
Notes: Step 1: Calculate cost of correspondence of each individual Fn obj. to Fn+1 obj.
Step 2: Calculate cost of correspondence for an Fn obj. splitting to many Fn+1 objs.
Step 3: Similarly compute cost of combining multiple Fn objs. to 1 Fn+1 obj.
Condition: The grey area is irrelevant (e.g. 1,2 can be corresponded to A,B from other matrix cells too).
Step 4: Green column denotes the exiting cost of any Fn obj.
Step 5: Green row denotes the costs of any obj. in Fn+1 entering.
Step 6: The Hungarian algo. will be used to find the minimum cost solution.

## Slide 18
But how to compute all these Costs in the correspondence matrix?
1,2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1,3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1,4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2,3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2,4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
3,4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1,2,3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1,2,4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1,3,4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2,3,4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1,2,3,4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
A,B | A,C | A,D | B,C | B,D | C,D | A,B,C | A,B,D | A,C,D | B,C,D | A,B,C,D
Entry |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Exit
 | A | B | C | D
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 
4 |  |  |  | 
To compute the ANSWER, we need a matrix of costs, which can be resolved by the Hungarian Algorithm
Notes: -> But what would goes in the cells of this table – what is the COST
-> So in case of SIFT, this would be L2 distance b/w SIFT feature descriptors
but we will take a PROBABILISTIC approach

## Slide 19: Parzen Window Estimates for Cost
Fn+1
B
C
Fn
1
How to use Shapes for Correspondence?
Parzen Window Estimate models the probability of ‘presence’ of an object
e.g.
How to compute the cost of object ‘1’ in Fn to object ‘B’ and ‘C’ in Fn+1?
Parzen Window Estimate as a cost metric
Notes: -> We propose Parzen Window Estimate as a COST metric
-> Parzen Window Estimate models the probability of ‘presence’ of an object while accounting for any motion that can occur.
-> Example: compute cost of corresponding obj. ‘1’ in Fn to obj. ‘B’ and ‘C’ in Fn+1
… an object splitting scenario?

## Slide 20: Parzen Window Estimates for Cost
Using 2D Gaussians, compute the Parzen Window Estimates for each object
How to use Shapes for Correspondence?
Notes: -> Using 2 Dimensional Normal Dist., compute Parzen Window Estimates for each obj. in the frame (shown for objects ‘1’, ‘B’, ‘C’)
-> On the two PW est. on the left note how uncertainty in motion as PLATEAUs with slopes

## Slide 21: Parzen Window Estimates for Cost
.*
=
Parzen Window Estimate of Object 1
combined Parzen Window Estimate of Objects B and C
correlated with …
equals …
Gives per pixel Probability distribution. Its normalized sum is our cost
How to use Shapes for Correspondence?
Notes: -> Probability distribution of ‘corresponding’ Object 1 to Objects B and C.
-> Normalizing the sum of probabilities by the total covered area will give the Cost

## Slide 22
…. BUT computing each Parzen Window Estimate is slow?
Can we skip computing irrelevant costs?
Notes: -> …. BUT the Hungarian Algorithm demands computing many costs
& computing each Parzen Window Estimate is slow?
-> Increasing no. of objects, there will be a COMBINATORIAL explosion
-> So is there a way to avoid computing all these costs?

## Slide 23: Steps to effective ‘Gating’
Original frame
minimizing the no. of computations of Parzen Window Estimates …
Step 1. Extract objects and dilate
Notes: -> Simplest way to work is to separate obj.s into different spatial regions.
-> So different far-off objects are not considered for correspondence.
-> Note for this to work – quick capture compared to motion

## Slide 24: Steps to effective ‘Gating’
1
2
3
4
5
6
Bg. subtration and connected component labeling
minimizing the no. of computations of Parzen Window Estimates …
Step 1. Extract objects and dilate

## Slide 25: Steps to effective ‘Gating’
1
2
3
4
5
6
minimizing the no. of computations of Parzen Window Estimates …
Dilate each object area
Step 1. Extract objects and dilate

## Slide 26
Step 2. Divide the frame into obj. Groups
Fn
Fn + 1
||
Note in Fn we have 4 connected groups whereas Fn+1 has 3
Notes: -> Explain why the region have become so bloated. ‘Gating’ technique explain!
-> The sign between is a pixelwise OR

## Slide 27
Step 2. Divide the frame into obj. Groups
Fn
Fn + 1
||
OR Result

## Slide 28
Step 2. Divide the frame into obj. Groups
Fn
Fn + 1
||
1
2
3
OR Result
Connected component labeling
Notes: -> I will call these connected regions as “GROUPS”
-> Note that, considering a constraint on the amount of motion, an ‘Or’ will result in the minimum number of possible groups
-> Note that the concept of groups is across 2 frames

## Slide 29
Advantages of dividing frames into Groups
It allows us:
Less objects per Hungarian graph, resulting in quicker computations.
Isolate the computation of far-away, un-related objects in the same frame
Stop the exponential rise of object combinations
Before ‘gating’, 15+ objects, not possible; now 40+ objects within 20 seconds.
Notes: -> Since Hungarian algorithm’s complexity is O(n3), smaller will be faster
-> Before employing this ‘gating’ technique, we were unable to compute frames with 15+ objects. Now frames with around 40+ objects are computed within 20 seconds.

## Slide 30
Step 3. Pick a Group and compute all Possibilities
Lets choose Group 3 (prev. slide) for our example →
0 14.7 -21.2 111.5
0 0 -29.6 36.6
0 0 0 -14.1
0 0 0 0
1 2 3 4
1
2
3
4
1
2
3
4
0 1 1 0
0 0 1 0
0 0 0 1
0 0 0 0
Step B: Compute the inter-object distances
Step A: Mask out all objs. of the group
Step C: Threshold it!
Step D: Compute Maximal Cliques
Clique 1 of objs. -> 1, 2, 3
Clique 2 of objs. -> 3, 4
Notes: -> So we separated out diff. obj.s into GROUPS (through Gating),
BUT can we reduce the computation in each group?
-> Main idea: obj. can split into or be combined from objects which are mutually nearby.
-> Note that this supposition is only there to speedup computation and might not always hold true.
-> Step B: note for quicker computation we can just compute the radial distance from the center
-> Explain distance, and threshold. Move motivation before explaining stuff

## Slide 31
Step 3 continued: compute psbs. of obj. regions
Step D: Computed the Maximal Cliques
Clique 1 of objs. -> 1, 2, 3
Clique 2 of objs. -> 3, 4
1
2
3
4
Step E: For every clique compute all sub-possibilities
For Clique 1 (1, 2, 3) we will have:
1, 2
2, 3
1, 3
Step F: Collect all possibilities from all cliques
1 1, 2 1, 2, 3
2 2, 3
3 1, 3
4 3, 4
Step G: Construct valid combinations
e.g. valid possibilities for Hungarian
Psb. 1 (1) (2) (3) (4)
Psb. 2 (1) (2,3) (4)
Psb. 3 (1,2,3) (4)
Notes: -> Step E: For every clique with more than 2 objs., compute all sub-possibilities
-> Step F: Collect all the possibilities from ALL the cliques, to get possible object splits/merges
-> Step G: BUT the problem is that all of these cannot be used in a single Hungarian graph (dependencies!).
Need to construct a list of all possibilities .
Each of these used separately in a Hungarian

## Slide 32
Motivation for Maximal Cliques
Eventually, Maximal Cliques gives a quick way to compute merges and splits for strongly connected (close-by) objects
Maximal Cliques helps break computation down to multiple smaller Hungarian graphs
Step 3 continued: compute psbs. of obj. regions
Notes: -> So maximal cliques is just a way to get groups of objects which can experience merges or splits.
-> After ‘gating’ objects into Groups, essentially, Maximal Cliques helps break computation down to multiple smaller Hungarian graphs
Rather than computing 1 large Hungarian graph (complexity of O(n3))

## Slide 33
D
A
B
C
4
1
2
3
Fn
Fn+1
Step 4: Compute Hungarian for every valid Fn, Fn+1 object combination
Step A: Choose a possible graph
1
4
2, 3
Entry
D A,B,C Exit
Fn Objects
Fn+1 Objects
Condition: Every graph will give the possibility of Entry and Exit to individual objects
Constraint 2: no. of groups in Fn+1 ≤ no. of individual objects in the Fn
Constraint 1: no. of individual objs. In Fn+1 ≥ no.of groups in the Fn
Notes: -> perform Maximal cliques, for both Fn and Fn+1 to make multiple Hungarian graphs.
-> So the idea would be to choose the graph that gives the lowest cost
-> Valid graphs need to have the following constraints (reduces no. of graphs):
-> Constraint 1: The no. individual objs. in the Fn+1 frame should be at-least as many as the no.of groups in the Fn frame
-> Constraint 2: no. group objs. in the Fn+1 frame should be at-most as many as the no. of individual objects in the Fn frame
-> Opportunity for an object from Fn to EXIT and an object in Fn+1 to ENTER

## Slide 34
Step B: Compute the correlation of Parzen Window Estimates for each location in the graph
Step a. Mask the needed obj.s
Step c. Correlation
Step b. Parzen Window Estimate
D
A
B
C
4
1
2
3
Fn
Fn+1
Step 4: Compute Hungarian for every valid Fn, Fn+1 object combination
Step A: Choose a possible graph
1
4
2, 3
Entry
D A,B,C Exit
Fn Objects
Fn+1 Objects
Notes: -> Step B: e.g. the red box cell will have the correlation value at row 1 (Obj. 1) and column 2 (Obj.s A,B,C) -> which is computed in the 3 steps given below (as described earlier)

## Slide 35
Step C: Compute Hungarian for the graph for the optimal solution
e.g. last slide would result in:
1 → Exit
4 → D
2,3 → ABC
To get the global optimal solution, compute Hungarian for all the possibilities found in Step 3

## Slide 36
Iterative Step: Repeat Step A, B, C for all possible groups from Step 3
1
2
3
4
Entry
D ABC Exit
1
2
3,4
Entry
A B CD Exit
. . .
. . .
Step D: Group’s solution from graph with lowest total Cost
Solution for this region:
1 → A
2 → B
3 → C
4 → D
Step C: Compute Hungarian for the graph for the optimal solution
e.g. last slide would result in:
1 → Exit
4 → D
2,3 → ABC
Notes: -> Step D: With this iterative step, a Group’s final solution comes from the graph having the lowest total Cost

## Slide 37
Cell motility
Basic techniques in Tracking
Solving for Occlusion in Actin-Myosin motility tracking
Shape aware Tracking in Bioimaging
Notes: 2nd part will involve generalized tracking – can be applied to anything

## Slide 38: Why Occlusions is a tough problem?
Notes: -> Show the sections of the video which are problematic
-> Three techniques

## Slide 39
Fn
Fn+1
Resolving Occlusions
How do you decouple the blue and red Actins in Fn in the merged object in Fn+1?
Notes: -> The question being how do you tell in which portion of the object in Fn+1 belongs to the red actin and which belongs to the blue Actin?

## Slide 40
Given the Parzen Windows of the Blue and Red Actins in Fn, the object in Fn+1 can be divided by checking the probability of each Actin’s presence
Parzen Window of Red Obj.
Parzen Window of Blue Obj.
Fn+1
Method 1: Parzen Windows
Notes: -> If we can advect the location of both the red and blue Actins to the next frame, we can simply assign pixels according to the respective Actins by seeing which Parzen window has a higher value at a certain pixel
-> The aim is to assign those pixels in the Fn+1 object to Blue Actin wherever pixels have higher probability to belong to Blue than Red Actin

## Slide 41
Parzen Window of the Blue object
Parzen Window of the Red object
the single combined object in Fn+1
disambiguation of the objs. according to who has higher Przn. Wndw. values
and …
mapped onto …
results in …
Method 1: Parzen Windows

## Slide 42
Moreover we have also experimented on differentiating between shapes in an occluded state using Shape Contexts [1]
[1] G. Mori, S. Belongie, J. Malik, “Efficient Shape Matching Using Shape Contexts,” IEEE Trans. PAMI, Nov. ’05.
Fn
Fn+1
Resolved Fn+1
Method 2: Shape Contexts
Notes: -> In the next few slides I will briefly give an overview of Shape Context and how they can be used in resolving occlusion events

## Slide 43
How Shape Context is used to keep merged objects separate?
So we have two (going to be merged) objects in Fn …
Fn
Fn+1

## Slide 44
… first, sampling the perimeter points of both objects
Compute the Shape Contexts of both the objects in Fn
by
Fn
How Shape Context is used to keep merged objects separate?
Notes: -> First step in Shape context – sample perimeter points

## Slide 45
… then by computing the log-polar graph of each sampled point
θ
log r
θ
log r
θ
log r
θ
log r
Fn
How Shape Context is used to keep merged objects separate?
Notes: -> Compute the log polar graph for each perimeter point
-> Notice while computing the log-polar graph, points for both objects are considered simultaneously

## Slide 46
Do the same for the single merged Fn+1 object
θ
log r
θ
log r
θ
log r
Fn+1
How Shape Context is used to keep merged objects separate?
Notes: -> Same thing done for Fn+1’s object

## Slide 47
How to divide the object in Fn+1 into the two Actins?
We take two points (P1 and P2) as an example …
P1
θ
log r
θ
log r
P2
Fn+1
How Shape Context is used to keep merged objects separate?
Notes: -> The aim is to associate every sampled perimeter point in Fn+1 to either of the two original objects in Fn
-> The association will decide which portion of the object belongs to which Actin

## Slide 48
Compare the log polar graph of P1 and P2 to every sampled perimeter point of both objects in Fn & try to find the closest match
θ
log r
θ
log r
θ
log r
θ
log r
θ
log r
θ
log r
P1
P2
Showing closest 6 matches
Fn
Matches!!
How Shape Context is used to keep merged objects separate?
Notes: -> The log polar graphs of P1 and P2 are compared to all log-polar graphs from Fn.
-> … comparison is done through Chi Squared distance between log polar graphs
-> The slide shows the 6 closest matches – note how all matches lie a certain proximity

## Slide 49
Fn
The results can be seen through quivers
All points in Fn+1 get associated to points in Fn
How Shape Context is used to keep merged objects separate?
Notes: -> Using this technique all points in Fn+1 get associated to points in Fn. Hence, Fn+1 has essentially been bifurcated into two objects!

## Slide 50
Fn+1
The final Result!
How Shape Context is used to keep merged objects separate?

## Slide 51
By repeating this process over time, while the objects are merged, we can keep merged objects separate.
Method 2: Shape Contexts
Link to failure case
Notes: -> So performing shape contexts over time preserves the identity of the two Actins. On a split we can then decide which object is which by seeing where have most of points ended.
-> This method fails in complete occlusions and cross-overs.

## Slide 52
Results on Actin and Myosin (proteins) interactions in an illuminated microscopic assay. Object merge/split disambiguation done through Shape Contexts
Method 2: Shape Contexts

## Slide 53
(Step 1)
(Step 2)
(Step 3)
A
B
(Step 4)
(Step 5)
Method 3: Spline Segmentation
Smooth and get labeled object
Skeletonize and create Splines
Synthesize skeletons at occlusions
Extend the splines to occlusions
Generate possible Actin regions
Notes: -> Still under experimentation | result of our experience. We think that the key is segmentation using information about the length and last known shape of the Actin
Conditions & clues
-> Actin can only be of a certain width
-> Regions of occlusions usually have different camera sensor response (increase in green layer)
-> Each Actin’s skeleton can have only two ends
-> They bend smoothly
Shows the major steps in segmenting a connected component label into different Actins in a single frame.
-> Step 1: smoothens the frame and thresholds to extracts a connected component label; which can contain a number of Actin filaments. -> Step 2: generates splines from the skeleton of the given connected component label
-> Step 3: computes the regions of possible occlusion, and then synthesizes Actin skeletons in these regions.
-> Step 4: associates the splines and skeletons generation Step 2 and 3B while keeping the bending of splines in check
-> Step 5: generates the possible segments as indicated by the output of step 4; this gives the Actins present in the connected component label.

## Slide 54: key Ideas
a region of occlusion is essentially missing information
first connect Actins where we feel there is no occlusion
if the object model is good, some guesses can be made about the shape of the object behind the occlusion.
Method 3: Spline Segmentation
Notes: -> So the region of occlusion is missing information. The segmentation technique has to guess about this region – but make informed guesses by looking at previous segmentations
-> first Actins are associated across the occlusion area – for this to happen reasonably a good object model is necessary (this job becomes increasingly difficult with increasing complexity of possible deformations in a non-rigid object)
-> (and can only undergo a limited amount of deformation)

## Slide 55
Link to preliminary results
Method 3: Spline Segmentation

## Slide 56
Q?
Thank you
Shape aware Tracking in Bioimaging